## Slide 1
SUBJECT :MR3691 ROBOTICS
Nehru Institute of Engineering and Technology
Department of Mechatronics Engineering
LECTURE 1
UNIT IV - ROBOT PROGRAMMING
TOPICS :INTRODUCTION- ROBOT PROGRAMMING
YEAR /SEMESTER :III /VI
PREPARED BY :Dr.SP.Arunkumar, Associate Professor

## Slide 2
Robot programming:
“Robot Programming is a art of teaching a robot online or offline a series of tasks to be performed with required accuracy, velocity and repeatability.”

## Slide 3: Robot Programming
The development of robot programming concepts is almost as old as the development of robot manipulators itself.
A characteristic feature of robot programming is that usually it is dealing with two different worlds, as shown in figure,
1) The real physical world to be manipulated.
2) Abstract models representing this world in a functional or descriptive manner by programs and data.

## Slide 4: General robot programming paradigm

## Slide 5: Methods of Training Robots
1. Lead through programming used for servo-controlled robots
Teach-by-guiding
Teach by teach- box methods
a. Point-to-point
- Move robot to each point in task and record it.
b. Continuous-path
- Move robot through entire task at normal speed while the robot records its position many times a second.

## Slide 6: Methods of Training Robots
3. Off-line programming used for servo-controlled robots
a. Transfer from another robot that already knows how to do task. b. operators write the task programs with step-by-step procedure in some programming language
4. Robot Simulation

## Slide 7
There are various methods which robots can be programmed to perform a given work cycle. We divide this programming method into four categories.
1. Manual method
2. Walkthrough method
3. Lead through method
4. Off-line programming

## Slide 8: Manual method
This method is not really programming in the conventional sense of the world. It is more like setting up a machine rather than programming. It is the procedure used for the simpler robots and involves setting mechanical stops, cams, switches or relays in the robots control unit. For these low technology robots used for short work cycles (e.g., pick and place operations), the manual programming method is adequate.

## Slide 9: Walkthrough method
In this method the programmer manually moves the robots arm and hand through the motion sequence of the work cycle.
Each movement is recorded into memory for subsequent playback during production. The speed with which the movements are performed can usually be controlled independently so that the programmer does not have to worry about the cycle time during the walk through. The main concern is getting the position sequence correct. The walk through method would be appropriate for spray painting and arc welding.

## Slide 10: Lead through method
The lead through method makes use of a teach pendant to power drive the robot through its motion sequence. The teach pendant is usually a small hand held device with switches and dials to control the robots physical movements. Each motion is recorded into memory for future playback during work cycle. The lead through method is very popular among robot programming methods because of its ease and convenience.

## Slide 11: Teach by guiding
It is some times also called as lead through programming. Primarily this method is highly suitable for programming the continuous path robots.
It can be done with simple equipment and controls. Also, the teaching is performed quickly and is immediately useful.
In the playback mode, the robot repeats the path and operations that were stored in memory during the teach operation.

## Slide 12: Teach by guiding
In some systems, it is possible to play back at different speeds than the speed that was used in the teach mode.
Each movement is recorded into the memory for the playback during production.

## Slide 13: Teach by guiding
A person doing the programming has physical contacts with the robot arm, actually gains control and walks the robot's arm through the desired positions.

## Slide 14: Teach by guiding
The main concern is on achieving the correct positioning sequences. Cycle time and speed can be changed later, when necessary.
A dead man’s control should be fitted for the safety reason.
Every operator motion is recorded and played back in the same manner, including unintended motions.

## Slide 15: Teach by guiding
Disadvantages to teach-by-guiding:
It is difficult to incorporate sensory information.
It cannot be used in some hazardous situations.
It is not practical in handling large robots.
Since teaching is performed manually, high precision in generating paths con not be achieved.
Synchronization with other operations/device/external sensor may be difficult.

## Slide 16: Teaching by teach - box method (Teaching and pendant control)
Teaching the robot via teach pendants that has toggle switches or contact buttons for controlling the movement of the robot.

## Slide 17: Teaching by teach - box method (Teaching and pendant control)
Moving the robot arm to each specific point manually and pressing a button to record the coordinates of that point do teaching in point-to-point systems.
Encoders, potentiometers, or other means does position measurement.
Large robot arms are often counterbalanced to make manual movement easier. Some large robots have an auxiliary lightweight arm that can be used for training or guidance.

## Slide 18: Teaching by teach - box method (Teaching and pendant control)
The teach pendant can control all axes of the robot arm in terms of position and movement velocity.
Pendant controls are especially useful for large robots that might otherwise be difficult to take through the training cycle.
They are also useful in applications in dangerous environments.

## Slide 19: Teaching by teach - box method (Teaching and pendant control)
In addition, they are more convenient for many purposes other than manual movement, so the use of pendant control has increased in the last few years.
The main disadvantage of this method is that the equipment is tied up in the programming stage.
However because of simplicity this method is widely accepted in industry, especially in PTP applications such as machine loading and unloading, spot welding, simple assembly tasks.

## Slide 20: Advantages and Disadvantages
Advantages:
• Shop personnel can readily learn it, does not require deeper programming experience
• Logical way to learn
Disadvantages:
– Production must be interrupted
– Teach pendant have limitations in the amount of decision making logic that can be incorporated into the program
– No interface to other computer subsystems in the factory (no CIM).

## Slide 22: On-Line/Lead -Through programming
Advantage:
  Easy
  No special programming skills or training
Disadvantages:
  not practical for large or heavy robots
  High accuracy and straight-line movements are difficult to achieve, as
  are any other kind of geometrically defined trajectory, such as circular
  arcs, etc.
  difficult to edit out unwanted operator moves
  difficult to incorporate external sensor data
  Synchronization with other machines or equipment in the work cell is
  difficult
  A large amount of memory is required

## Slide 23: Off- line programming
This method involves the preparation of the robot program off-line, in a manner similar to NC part programming.
Off-line robot programming is typically accomplished on a computer terminal.
After the program has been prepared, it is entered in to the robot memory for use during the work cycle.
The advantaged of off-line robot programming is that the production time of the robot is not lost to delay in teaching the robot a new task.

## Slide 24
Programming off-line can be done while the robot is still in production on the preceding job. This means higher utilization of the robot and the equipment with which it operates.
Another benefit associated with off-line programming is the prospect of integrating the robot into the factory CAD/CAM data base and information system.

## Slide 25: The advantages of offline programming
1. It can prepare programs without using the robot, so that the robot is available for other uses.
2. Previously worked-out procedures and routines can be incorporated in the program.
3. Layout and cycle time of the operations can be optimized in advance.

## Slide 26: The advantages of offline programming
4. Sensors can be used to interact with external environment, and appropriate action can be taken in response.
5. Existing Computer Aided Design (CAD) and Computer Aided Manufacturing (CAM) information can be incorporated into the control functions through proper interfacing.

## Slide 27: The advantages of offline programming
7. Robots can be used to manufacture individual units by calling on previously developed routines. It would be impractical to do this by guiding and attempting to match different paths.
8. Programs can be run in advance to simulate the movements actually programmed without incurring the risk of damage.

## Slide 28: Limitations of programming languages
Existing robot programming languages often have limited ability to use subroutines and do logic testing
Some of the early generation controllers lack the memory capacity to hold such large programs.
Languages are difficult to learn.
Languages change radically over time. Probably the biggest problem with robot programming languages is that Robot manufacturers constantly obsolete their existing languages when they introduce new generations of robot controllers.