## Slide 1
SUBJECT :MR3691 ROBOTICS
Nehru Institute of Engineering and Technology
Department of Mechatronics Engineering
LECTURE 1
UNIT IV - ROBOT PROGRAMMING
TOPICS :INTRODUCTION- ROBOT PROGRAMMING
YEAR /SEMESTER :III /VI
PREPARED BY :Dr.SP.Arunkumar, Associate Professor

## Slide 2: Computer like Robot Programming Languages : Basic Elements
Define Constants and Variables
Motion commands (coordinate systems)
End Effectors Commands
Sensor Commands
Program Control Commands
Communications Commands
Monitor Mode Commands

## Slide 3: Robot Programming Languages
WAVE
  Developed at Standford
  Demonstrated a robot hand-eye coordination in the machine vision robot
  Trajectory calculations through coordination of joint movements, end-effector positions and touch sensing
  Algorithm is too complex and not user friendly
AL
  Later developed at Standford
  The language can implement various subroutines, involving activities between the robot and its surroundings.

## Slide 4: AL (Assembly Language)
AL is a high-level programming system for specification of manipulator tasks such as automatic assembly in production line manufacturing.
AL has a considerable effect on other languages and has emerged as one of the leading contenders for a common robotic language.
It was developed at Stanford University in 1974 and has been improved and tested since then.

## Slide 5: AL (Assembly Language)
It has an ALGOL-like source language, a translator to convert programs into run able code, and a runtime system for controlling manipulators and other devices. Trajectory calculations are done at compile time and are modified during runtime as necessary.
Two or more objects can be handled as one by the use of AFFIX commands that cause them to appear as one object.

## Slide 6: AL (Assembly Language)
Force sensing and compliance are implemented by a number of subroutines and by condition monitor statements in the syntax of the language.
There are signal statements and wait statements available when one process must wait for the completion of another process. These and other statements make possible the coordinated operation of two or more robot arms.
Arm and hand movement commands are available to control moves, velocities, forces, and torques.

## Slide 7: Robot Programming Languages
VAL
  Popular textual robot language developed by Unimation Inc. for the PUMA series of robots.
  Victor Sheinman developed VAL languages.
  Later VAL II is developed
  It provides arm movement in joint, world and tool coordinates, gripping and speed control.
AML
  Developed by IBM
  It is possible to interface other programming languages.

## Slide 8: AML (A Manufacturing Language)
AML was developed in 1976 at IBM’s T.J. Watson Research Labs for assembly related tasks.
AML provides a systems environment in which different user robot programming interfaces may be built.
It supports joint space trajectory planning, subject to position and velocity constraints. Relative and absolute motion can be handled, and sensor monitoring can interrupt motions as necessary.

## Slide 9: AML (A Manufacturing Language)
The most unique capability of AML is its operations on data aggregates, so that many operations on vectors, rotations, and coordinate frames can be handled as multiple operations in one command. This capability makes the language more difficult to understand but simplifies programming and control.

## Slide 10: Robot Programming Languages
MCL
  Developed by McDonnel-Douglas at US Air force
  Modification of APT (Automatically programmed Tooling) languages used for CNC
RAIL
  Developed by Automatix for robotic assembly, inspection, arc welding and machine vision
  A variety of data types as used in PASCAL can be used

## Slide 11: RAIL
It was developed by Automatix Inc., for the control of both vision and manipulation.
It contains a large subset of PASCAL commands and can handle a variety of data types.
An interpreter is used to convert the language constructions to machine language commands. Inspection, arc welding and vision operations are supported by language capabilities. It is run on a powerful Motorola 68000 system.

## Slide 12: MCL
MCL was developed in 1978 by McDonnell-Douglas in conjunction with Cincinnati Milacron for an Air Force ICAM Project.
This language is based on APT, the control language for numerically controlled (NC) machine tools used in CAM.
One of its advantages is that a large number of programmers already use APT in CAM applications.
APT has specific constructs to specify POINTS, LINES, PATTERNS, and so on, which are useful in enabling robots to communicate and cooperate with machine tools.

## Slide 13: RPL
RPL was designed at SRI (Stanford Research Institute) specifically for unskilled programmers, factory production engineers, line foremen, and so on.
It is a low level language.
It has a compiler to produce interpretable code from programs and an interpreter for that code. The language is implemented as subroutine calls, so that it is modular and flexible in use.

## Slide 14: RPL
It has been used to control a Unimation PUMA 500 arm and the Machine Intelligence Corporation (MIC) vision module.
Some of the ideas of the LISP language are used but are organized into a FORTRAN-like syntax. (LISP is a language designed for artificial intelligence use. It is primarily recursive and is especially well adapted to handling lists of information.)

## Slide 15: ADA
ADA was developed by Ada Lovelace for the Department of Defense (DOD) in 1978.
It has been specified by DOD as the sole system implementation language for the programming of real-time embedded systems.
Chief advantages of ADA are the powerful data structures provided the ability to separate control operations from data operations, and the inherent capability for concurrent operation of many tasks.

## Slide 16: ADA
Concurrent operation is an important requirement for the efficient use of multiple robots and other equipment.
The ADA is well suited to the control of manufacturing cells using robots.
In addition, ADA is expected to provide code that is easily transferred between computers and can be easily maintained.

## Slide 17: Robot Programming Languages
HELP
  Developed by General Electric Company
  It has capability to control two robot arms at the same time
JARS
  Developed by NASA’s JPL.
  The base language is PASCAL
  It can be interfaced with PUMA 6000 robot
RPL
  Developed by SRI international.
  The basic ideas of LISP language have been organized into a FORTRAN – like syntax
  It can be interfaced with PUMA 500 robot

## Slide 18: PLAW (Programming Languages for Arc Welding).
A robot manufacturing company, Komatsu developed it for its series RW Cartesian robots, equipped with arc current and television.
This is a low-level language specifically developed to program an adaptive welding robot. It primarily serves to simplify the programming of complex operations.
In contrast to AL, this language does not call for the use of a large computer (it can well be implemented with a microcomputer).

## Slide 19: PLAW (Programming Languages for Arc Welding).
PLAW includes the following instructions:
-Robot motion control (point-to-point, using various interpolation techniques)
-Control of welding equipment
-Control of peripherals (by turning ON and OFF the respective channels)
-Control of sensor systems
-Service instructions
-Conditional and unconditional jump instructions. Conditional jump instructions check the status of flags and perform the respective branch action

## Slide 20: PASCAL
It is a standard programming language developed by Blazie Pascal for data processing that uses structured statements to organize the program in a modular and efficient way.
The structured statements force the program into separate modules to reduce the number of branches.
Each module is self-contained and can be entered only at the top and exited only at the bottom, so that errors due to branching mistakes are easier to catch and eliminate.

## Slide 21: PASCAL
Data types are the descriptors that identify elements in the language such as INTEGERS, REAL NUMBERS, and CHARACTERS.
It is a well-known and widely used language, and was chosen as the basis for several robot languages.

## Slide 22: PAL
Richard Paul, added capabilities to PASCAL to WAVE and the AL language provide a new type of programming language PAL.
PAL, the Pedagogic Algorithmic Language.
This allowed them to take advantage of the proven, well-known PASCAL language and yet provide new capability.
In the PAL data structure, the relationship between the arm and the object can be given explicitly by the use of homogeneous matrix transforms. Every motion statement in PAL causes the manipulator position and orientation to be specified in an equation representing a closed kinematic chain.

## Slide 23: PAL
An interesting and potentially valuable capability of PAL is the ease with which unknown points can be picked up from a task and incorporated into the program. Every motion statement in PAL causes the solution of homogeneous equations that represent the position of the kinematic chain of links and joints in the arm.